# Normal lines
Must be enclosed by a Motion Control Block.
The pattern for normal lines is Accelerate, SETSPD(low), MOVEREL, SETSPD(high), MOVEREL, SETSPD(low), MOVEREL, Decelerate.
Command	Description
Accelerate	Specifies that the following SETSPD command, Initial speed is the starting speed, and Max speed is the final speed, for the following MOVEREL
SETSPD	Sets an initial and maximum speed for the next head movement. / If in Accelerate phase, movement starts at Initial speed and ends at Max speed / If in Decelerate phase, movement starts at Max speed and ends at Initial speed
MOVEREL	Move the head by dx and dy
Decelerate	Specifies that the following SETSPD command, Maximum speed is the starting speed, and Min speed is the final speed, for the following MOVEREL

A sample of a normal line is
a88: ACCELERATION Acceleration=Accelerate
a90: SETSPD Initial speed=1041 Max speed=20833 Acceleration=104164
aa0: MOVEREL n=772 dx=2078 dy=0
ab0: SETSPD Initial speed=20833 Max speed=20833 Acceleration=104164
ac0: MOVEREL n=772 dx=16676 dy=0
ad0: ACCELERATION Acceleration=Decelerate
ad8: SETSPD Initial speed=936.875 Max speed=20833 Acceleration=104164
ae8: MOVEREL n=772 dx=2079 dy=0

Outstanding queries
1. How are low and high determined?
2. We have interpreted the Initial speed, Max speed and Acceleration parameters as Floats. The values here seem unfeasibly high. There must be some sort of scaling involved.
# Engraving
Are not enclosed by a Motion control Block
The pattern for engraving is a single ENGACD & PWRSPD5 followed by
ENGLSR, ENGMVX, ENGMVY for each line of the engraving
Command	Description
ENGACD	The distance in steps of the initial acceleration phase, and the final deceleration phase
PWRSPD5	Sets the cutter power & speed
ENGLSR	A list of step lengths – the first is an On time, the second an Off time. Each step length is encoded in 1 word. On is LS 2 bytes, Off is MS 2 bytes.
ENGMVX	Causes engraving to occur according to preceding ENGLSR. dx is the total width of the engrave line. If negative, it is in the reverse direction.
ENGMVY	dy is Engrave movement in the Y direction

A sample of an engraved line is
aa8: ENGLSR List of steps=List of 4 On/Off steps 1260/1260 1260/1260 1259/1260 1260/13
ac0: ENGMVX Axis=4 dx=12346
acc: ENGMVY Axis=3 dy=63

Outstanding queries
1. How is ENGACD parameter determined? Probably determined by table for engraving speeds. For the test card we will need to reset ENGACD before each box.
2. Some of the PWRSPD5 parameters are not well understood. Corner PWR % Irrelevant) and Max PWR % are understood. The last 3 are not, and may or may not be relevant. What are they? We don’t have a 2 head cutter, so I’ve ignored PWRSPD7.
3. And the BIG question – Can I make a subroutine for a single cell, and call it 100 times? The ‘parameters’ for a cell subroutine are x, y, power, speed and ENGACD. The GOSUBn command supports a start position as a parameter.